## System report
Printout of important system data

SYSTEM - REPORT

DATE: 2003/04/09 23:23

SYSTEM: AC-4
SERIAL NO.: 1234567
SOFTWARE: 11.02.12

OPTIC 1: 80 30005 (162)
OPTIC 2: 62 29984 (169)
OPTIC 3: 85 29766 (153)
OPTIC 4: 50 29793 (155)

TEMPERATURE CV: 39.2 °C
TEMPERATURE PT: 37.0 °C
TEMP.FACTOR 1: 34302
TEMP.FACTOR 2: 34310

CONTRAST: 225
MIXER: 200
VMAX: 2

OFFSET X: 1 -2 0 0
OFFSET Y: 3 1 0 -5
OFFSET Z: 0 13 0 850
OFFSET M: 4
OFFSET P: 0

SYSTEM WATER: 108 ml
NEEDLE TIMER: 23%
SYRINGE TIMER: 6%
PT COUNTER: 344
PTT COUNTER: 6
FIB COUNTER: 302
ANALYSIS COUNTER: 1079

OPTICS : 80 30005 (162)
   80 = Digital value when LED is off
   30005 = Digital value when LED is on
   162 = Amplification factor

Temperature cuvette
Temperature PT reagent
Digital value of temperature CV.
Digital value of temperature PT.

Display contrast
Reagent mixing speed
Robot speed (1=min, 2=normal and 3=max)

Needle Position for Wash , Reagent,Cuvette & Patient
   X-Offset = left/right
   Y-Offset = forward/backward
   Z-Offset = up/down
Motor Adjustment
CAP PIERCING height

Remaining system liquid
Age of needle: 0% = new
Age of syringe: 0% = new
Number of counted PTs
Number of counted PTTs
Number of counted FIBs
Number of all tests carried out